## Slide 1: Internet Connectivity out of Ireland
Marie Armstrong
Vitali Panov
Ronan Moriarty

## Slide 2: Topics Covered
HEAnet
INEX
Ten-155
Traceroutes

## Slide 3: HEAnet
National Research Network
Internet connectivity to Third Level institutions
37 member institutions
10 Mbps link to Ten-155
2Mbps link to JA.net
24Mbps link to UUnet
key role in development of INEX

## Slide 4: INEX
Previously ISPs routed though New York
Interconnect Irish ISPs
ISPs must have independent external connectivity
  typically to MAE-East

## Slide 5: Ten-155
Largest Pan-European Network
Connecting research institutions
Replaces Ten-34
155 Megabits/sec across 16 countries
Access in Ireland through HEAnet

## Slide 6: Traceroute from www.infn.it
traceroute to 212.2.170.75 (212.2.170.75), 30 hops max, 40 byte packets
1 gw-lanserver (131.154.1.9) 1 ms 1 ms 1 ms
2 rc-cnaf.bo.garr.net (193.206.128.17) 2 ms 2 ms 1 ms
3 rt-rc-2.bo.garr.net (193.206.134.157) 2 ms 2 ms 2 ms
4 mi-bo-2.garr.net (193.206.134.5) 7 ms 7 ms 7 ms
5 garr.it.ten-155.net (212.1.196.25) 8 ms 9 ms 8 ms
6 it-se.se.ten-155.net (212.1.192.94) 61 ms 62 ms 61 ms
7 stockholm5.se.att-unisource.net (212.1.194.26) 63 ms 62 ms 62 ms
8 Fddi10-0.GW2.STK2.Alter.Net (194.68.128.23) 63 ms 63 ms 63 ms
9 431.ATM6-0-0.CR1.STK2.Alter.Net (146.188.5.77) 63 ms 63 ms 63 ms
10 219.ATM8-0-0.CR1.LND3.Alter.Net (146.188.6.146) 98 ms 99 ms 97 ms
11 160.ATM9-0-0.CR1.DUB1.Alter.Net (146.188.2.225) 107 ms 110 ms 109 ms
12 311.ATM8-0-0.GW1.DUB1.Alter.Net (146.188.2.162) 109 ms 108 ms 109 ms
13 Ocean-gw.customer.ALTER.NET (146.188.35.154) 110 ms 111 ms 109 ms
14 212.2.162.193 (212.2.162.193) 81 ms 81 ms 81 ms
15 212.2.162.74 (212.2.162.74) 80 ms 81 ms 80 ms
16 212.2.170.75 (212.2.170.75) 206 ms 200 ms 211 ms

## Slide 7: Traceroute from Paris
traceroute to 212.2.170.75 (212.2.170.75), 30 hops max, 40 byte packets
1 cisco.brainstorm.fr (193.56.58.254) 3.478 ms 2.463 ms 2.361 ms
2 194.51.174.13 (194.51.174.13) 86.620 ms 24.537 ms 29.521 ms
3 archives-villette.grolier.fr (194.117.192.118) 37.371 ms 28.955 ms 24.243 ms
4 ARC4-S-5-1-1.rain.fr (195.101.9.217) 24.761 ms 36.872 ms 31.729 ms
5 RASG2-POS-1-2.rain.fr (194.51.221.73) 37.529 ms 28.486 ms 24.079 ms
6 RBS2-p4-0-0.rain.fr (194.250.88.134) 39.473 ms 136.653 ms 36.373 ms
7 gip-raspail-1-fastethernet0-0.gip.net (204.59.18.193) 38.282 ms 115.939 ms 250.552 ms
8 Serial2-7.BR1.PAR2.ALTER.NET (146.188.32.85) 39.010 ms 38.633 ms 32.683 ms
9 103.at-1-0-0.XR2.PAR2.Alter.Net (146.188.11.122) 40.843 ms 41.208 ms 25.318 ms
10 194.ATM1-0-0.CR2.PAR2.Alter.Net (146.188.10.78) 101.687 ms 116.918 ms 102.184 ms
11 218.ATM5-0-0.CR2.LND3.Alter.Net (146.188.6.178) 56.903 ms 112.357 ms 93.712 ms
12 160.ATM8-0-0.CR2.DUB1.Alter.Net (146.188.2.237) 131.464 ms 131.569 ms 121.204 ms
13 412.ATM9-0-0.GW1.DUB1.Alter.Net (146.188.3.18) 135.848 ms 111.102 ms 134.320 ms
14 Ocean-gw.customer.ALTER.NET (146.188.35.154) 66.616 ms 65.623 ms 59.943 ms
15 212.2.162.193 (212.2.162.193) 52.636 ms 63.641 ms 195.615 ms
16 212.2.162.74 (212.2.162.74) 52.349 ms 63.396 ms 59.805 ms
17 212.2.170.75 (212.2.170.75) 191.593 ms 196.584 ms 187.404 ms

## Slide 8: HEAnet - UUnet: 24Mbps (NY)

## Slide 9: INEX (Esat) 2048 kbps (Dublin)
Max Speed: 256.0 kBytes/s (propPointToPointSerial)

## Slide 10: Ebone - European Backbone